Model 3311, Gonset Inc., Waterproof Elect. Co.; Burbank (CA)

| Country: United States of America (USA) Manufacturer / Brand: Gonset Inc., Waterproof Elect. Co.; Burbank (CA) |  |
| --- | --- |
| Year: 1959 | Type: Car Radio |
| Valves / Tubes | 7: 12EC8 12EC8 12EZ6 12AD6 12EZ6 12EK6 12AL5 |

| Principle | Superhet with RF-stage; ZF/IF 10700 kHz; 1 AF stage(s) |
| --- | --- |
| Tuned circuits | 11 FM circuit(s) |
| Wave bands | FM Radio only |
| Details | Converter |
| Power type and voltage | Storage Battery for all (e.g. for car radios and amateur radios) / 12 Volt |
| Loudspeaker | - - No sound reproduction output. |
| Power out |  |
| from Radiomuseum.org | Model: 3311 - Gonset Inc., Waterproof Elect. |
| Material | Metal case |
| Shape | Miscellaneous shapes - described under notes. |
| Dimensions (WHD) | 6x4x7inch / 152x102x178mm |
| Notes | The Gonset Model 3311 is a 12Vdc Operated Universal Type Automobile FM Converter. Demodulated FM-AF modulates a low power BC oscillator at about 800 kHz for feeding an AM-only car radio. Uses seven low voltage 'Space Charge' tubes (12V plate voltage) that were engineered in 2nd half of the 50's to avoid use of 'vibrators', before that reliable (and not too expensive) transistors were available (especially RF). The converter could be screwed on the bottom side of the dashboard (faceplate front), or directly on the dashboard itself, when suitable space and location are available. |